## Slide 1
AMT PROJECT

## Slide 2
H4
H5
H6
H2
H3
H1
R
N
A
M
+
-
MCU
LOGIC
CIRCUITRY
CONNECTOR
A1
A2
A3
A4
Protection circuitry
12V
GND
Switching
Regulator (12V to 5V)
Note: H* are hall effect sensors.
Proposal 1: Hall Effect sensor

## Slide 3: Hall Effect sensor based AMT
In this method, we will be using 6 hall effect sensors to determine the positions of gear lever.
The outputs of hall effect sensors are given to Microcontroller. Based on the inputs received from hall effect sensor, the desired output will be obtained.
To obtain the desired logic levels at the output, logic circuitry is added.

## Slide 4
R
N
A
M
+
-
MCU
LOGIC
CIRCUITRY
CONNECTOR
A1
A2
A3
A4
Protection circuitry
12V
GND
Switching
Regulator (12V to 5V)
Magnetometer
M1
SPI
Proposal 2: Magnetometer

## Slide 5: Magnetometer based AMT
In this project, we will be using 3D magnetometer to determine the positions of the gear lever.
Magnetometer communicates with microcontroller using SPI protocol.
Magnetometer sends different data at each position. Based on the data received, the microcontroller will be programmed to give the desired output.
To obtain the desired logic levels at the output, logic circuitry is added.

## Slide 6: Comparison between HES and Magnetometer
HALL EFFECT SENSOR | MAGNETOMETER
Six Hall effect sensors are used to determine the positions of gear lever. | One magnetometer is enough to determine the positions of gear lever.
Calibration is not required | Calibration is required
Cost of HES PCBA is less compared to MAGNETOMETER PACBA | Cost of magnetometer PCBA is more compared to HES PCBA. (Unit price of sensor is around $5 even if we are going to procure 10000MOQs)

## Slide 7
Thank You